## Slide 1
WebAudio Synthesis of Japanese Cicada Calls:Acoustic Features and Modeling
Acoustic Characteristics of Major Cicada Calls (Minminzemi,Tsukutsukuboushi, Kumazemi)
The calls of Japanese cicadas are remarkably loud and cover broad frequency ranges, with each speciesproducing a distinct pattern and timbre. Spectral analyses show that cicada calls are rich in highfrequencies (often several kilohertz), and different species partition the acoustic spectrum and timestructure uniquely
1
2
. Below we summarize the key acoustic features of three prominent species:
• Minminzemi (ミンミンゼミ) – The call is famous for its “Meeen…min-min-min” pattern.Acoustically, Minminzemi’s song is intermittent and concentrated in the mid-high frequency bandaround ~3–6 kHz
followed by a series of shorter “min-min” pulses with a brief gap between them
a cyclic amplitude modulation. Spectrograms show energy primarily in the few-kHz range (someharmonics can extend beyond 10 kHz), and a clear on-off envelope corresponding to thealternating long/short segments
which may be due to prominent spectral bands (formant-like peaks) in its ~4–6 kHz region
analysis by Sound One found the dominant frequency around 3–6 kHz, a bit lower in pitch thanthe continuous buzz of Aburazemi
makes it feel less incessant than species with continuous trills.
1
. Each phrase typically starts with a sustained “Meeen” (a longer pulse)
. This results in
1
1
3
. Minminzemi’s call sounds slightly “nasal” or vowel-like,
. An
. The call’s intermittent nature (pauses after the “Meeen”)
4
1
1

## Slide 2
Spectrogram of a Minminzemi call. Time progresses left to right, frequency (Hz) on vertical axis. Brightbands around 4–6 kHz indicate the main energy. The repeated vertical striations show the pulsed “Meeen… min-min-min” pattern (loud segments separated by pauses)
1
3
.
• Tsukutsukuboushi (ツクツクボウシ) – This late-summer cicada produces a distinctive two-partcall often transcribed as “O-shī… tsuku-tsuku-bōshi!”. The call begins with an introductory
. Acoustically, Tsukutsukuboushi’s call covers an exceptionally wide frequency span – one
analysis found significant energy from about 1.7 kHz up to 15 kHz during a single call
dominant frequency is around ~6.3 kHz on average, but the spectro-temporal pattern clearlysweeps upward in pitch as the call progresses
contains more low-frequency energy (around a couple kHz) and the later portion adds more high-frequency components (well into the ultrasonic range)
change from the “tsuku-tsuku…” part to the high-pitched “...bōshi!” part. The transition infrequency content is so pronounced that young people with good high-frequency hearing mayperceive parts of the call that older listeners cannot (since energy extends to ~15 kHz)
time structure is also complex; unlike other cicadas, Tsukutsukuboushi’s song has a mid-call
respond differently to the first vs. second part of the call
phrase (“ooshīn, tsuku-tsuku…”) and then “tsuku ryōshi” finale, during which the pitch notably rises
5
2
. The
. In other words, the early part of the call
. This corresponds to the perceptual
2
2
2
. The
modulation (a “key change”) which is biologically significant – experiments show male cicadas
5
. Overall, its call is rhythmic and
“mysterious”, starting low and ending in an intense, high-pitched crescendo.
Spectrogram of a Tsukutsukuboushi call. The frequency content spans from ~1–2 kHz (green-yellowregions at the beginning) up to ~15 kHz (bright red band toward the end). The upward shift in dominantfrequency (from ~1.7 kHz early to ~6–15 kHz later) is clearly visible, corresponding to the call’s pitch risingin the second half
2
. Such broad frequency coverage and changing pitch are unique to this species.
• Kumazemi (クマゼミ) – The largest cicada (often called the “bear cicada”) has an extremely loud,piercing buzz “SHAaAA…SHAaAA…”. Its call is characterized by a continuous, relativelyunmodulated roar compared to the above species
strong energy in the range of roughly 2 kHz up to 10 kHz, which is exactly the range where humanhearing is most sensitive
or Tsukutsukuboushi, the Kumazemi’s sound has less obvious rhythmic segmentation or pitchchange; it’s more of a steady “shaaa” that may repeat with short pauses. Acoustic measurementsconfirm Kumazemi’s call is broadly spread across frequencies (nearly uniform from ~2–10 kHz), without the distinct low vs. high-band partition seen in some other cicadas. There may be
two gentle spectral peaks (one in the mid (~4–6 kHz) and another in upper (~8–10 kHz) ranges),but overall it’s a wideband “hiss”
might produce bursts or pulses at a high repetition rate (dozens of pulses per second), which fuseinto a continuous buzzing sensation
dramatic rise or dynamic changes of Aburazemi or Minminzemi; instead it calls in a steady
6
. In terms of spectrum, Kumazemi produces
. This is why its chorus sounds so overpowering. Unlike Minminzemi
7
7
8
. Temporally, Kumazemi calls can have a fast cycle: the insect
. One observation noted that Kumazemi lacks the
6
rhythm (often transcribed “shuwa-shuwa-shuwa…”) that, while extremely loud, is rather
2

## Slide 3
6
monotonous and “matter-of-fact” in its delivery
. The short cycle and relentless repetition
contribute to the impression of oppressive summer heat that this species’ chorus often evokes.
6
Prior Research on Cicada Call Synthesis and Modeling
Researchers have studied cicada sounds both to understand their production and to synthesize or
model them for musical and acoustic applications. Two main approaches emerge in the literature:physical (bioacoustic) models that simulate how the insect produces sound, and signal-basedsynthesis that replicates the sound’s spectral patterns. Key studies and techniques include:
• Physical Modeling of Cicada Sound Mechanism: Smyth and Smith (2001) developed abioacoustic model of a cicada’s sound-producing mechanism
sound can be modeled with a primary resonator (the tymbal mechanism) and a secondary. Their model implemented the
cicada’s “dual-resonator” system: each time a timbal rib buckles (producing an impulse), it is fedinto two resonant filters – one representing the vibrating tymbal plate and another representingthe Helmholtz-like abdominal cavity
muscle contraction, the model produces a series of impulses that excite these resonators,mimicking a natural chirp. This work resulted in The Tymbaline synthesizer, a real-time interactivecicada sound instrument in Pure Data (Pd)
example, parameters like the changing effective mass and frequency as each rib buckles were
included to simulate the slight downward shift in frequency observed during an actual cicada’srib-buckling sequence
parameters (spring stiffness of ribs, resonator tuning, etc.) affect the sound
for faithful synthesis.
• Signal-Based and Procedural Synthesis: In practice, directly simulating every rib click andresonance can be computationally heavy. Audio engineers like Andy Farnell have proposed more
cicada’s call, being a dense cloud of rapid clicks, can be efficiently approximated using filtered. He observed that real cicada chirps show two prominent
frequency bands (in a recorded example, about 5–6 kHz and 7–8 kHz, with a notch around ~6.5kHz) produced by the insect’s dual resonators
modes explicitly, one can start with a broadband noise source and then pre-filter it to constrainmost energy into the cicada’s known frequency band (for instance, ~5–8 kHz)
“killing” frequencies outside the key band to avoid muddying the timbre, since extraneous low-frequency components can cause unwanted modulation artifacts in the resulting sound
you have noise shaped into the appropriate band, the rhythmic structure of the call can beimposed by amplitude modulation or gating. Farnell’s analysis of a North American cicadashowed the call consisted of rapid bursts: about 5 bursts in 0.2 s (i.e. ~25 Hz repetition) for thecoarse rhythm, with each burst containing a train of micro-clicks at ~1 kHz rate
synthesis, this inspired a two-tier modulation: a low-frequency oscillator or envelope to create the25 Hz chirp cadence, and a higher-frequency element to impart a slight “buzz” texture within eachchirp. His approach produced a realistic cicada by using a noise-based exciter (instead ofindividually timing dozens of clicks) fed through a couple of resonant bandpass filters to createthe dual-peaked spectrum
cicada-like. A recent study by Matsumura (2022) in Japan similarly used physical modeling
built on Farnell’s cicada patch in Pd, adjusting parameters to emulate Japanese species like
9
. They identified that a cicada’s
10
11
resonator (the abdominal air sac) working in tandem
10
12
. By sequentially buckling multiple ribs during one
13
. The physical model approach is quite detailed: for
14
12
. Such models have clarified how slight adjustments in physical
– valuable insight
15
procedural solutions for cicada sounds. In “Designing Sound” (2010), Farnell notes that a
16
noise and strategic modulation
17
. Instead of simulating dozens of resonant
. Farnell suggests
. Once
18
18
19
20
. In
16
. This is far more CPU-friendly while still sounding convincingly
synthesis to recreate insect sounds, treating the cicada as an “organic synthesizer.” Matsumura
3

## Slide 4
21
22
Minminzemi and Higurashi (evening cicada)
simulate the timbral evolution of the call
control the relative level of tonal hum vs. noise, the envelope shape of the “Meeen” vs “min-min”sections, and the center frequency of bandpass filters to match the insect’s 3–6 kHz energy band.Such research demonstrates that combining vibratory models (for periodic components) with
. The Pd model included a mix of an oscillator
. For example, in his Minminzemi patch, one can
component (for tonal vibrations) and a noise component, plus resonant filters and envelopes to
21
23
procedural noise (for dense clicks) is an effective strategy in cicada sound synthesis.
Cicada Sound Production Mechanism: Biology and EngineeringInsights
Understanding how cicadas actually produce sound provides vital clues for modeling their calls. Cicadasuse a specialized organ called the tymbal, a stiff membrane with rib-like bands, to generate sound. Eachtymbal is a corrugated dome that buckles inward when a strong muscle in the cicada’s abdomencontracts, then pops back out when the muscle relaxes
fast, producing a loud click each time. A male cicada has two tymbals (one on each side of the abdomen)that can buckle in rapid succession, yielding a high repetition rate of clicks
one muscle contraction is often called a “chirp” or pulse train. Notably, the inward buckle and theoutward snap both produce sound – effectively two clicks per cycle
muscles in a steady rhythm, these clicks blur together into the continuous buzzy tone we recognize.
However, the raw clicks alone are not the full story. Cicadas have an internal acoustic resonator: an air-. The rapid
tymbal clicks drive this air cavity into vibration. The air sac is tuned to about the same natural frequencyas the tymbal itself, reinforcing the sound via resonance
excitation (broadband impulses), and the abdominal cavity filters and amplifies those impulses into aringing tone. The coupling of two resonators – one mechanical (tymbal) and one acoustical (air sac) – iskey to cicadas’ sound production
species, the tymbal’s resonant frequency and the abdominal cavity’s resonant frequency are very close,yielding an efficient transfer of energy and a sharp, strong tonal peak
more pure tone than a click alone could produce.
Additionally, cicadas have large tympana (eardrum membranes) on the sides of the abdomen that serveas sound radiators. These tympana (which in the living cicada are actually part of the hearing organ, butdouble as an “output speaker”) are much larger in area than the tymbal, and they effectively act as animpedance matching device to efficiently broadcast the sound into the air
that the big, thin tympana give the abdominal cavity resonator a large opening to vent sound, making theinsect’s song extraordinarily loud for its size
oscillator (tymbal ribs) generates high-frequency energy, an acoustic amplifier (air sac) boosts and tunesit, and a radiator (tympana aperture) projects it outward. This synergy explains how cicadas achievesound pressure levels around 100 dB SPL or more at close range – among the loudest of all insects.
In summary, from an engineering perspective, a cicada is like a tiny electromechanical transducer: themuscle’s mechanical energy is transduced into sound through the tymbal (a ridged drum skin) andshaped by a resonant amplifier (abdominal cavity). Each species tweaks this basic design by varying thesize of the air sac, the stiffness and geometry of tymbal ribs, etc., thereby setting its unique songfrequency. For example, larger cicadas (like Kumazemi) tend to have slightly lower dominant frequencies(in the few kHz range) while smaller cicadas (like Niini-zemi) reach higher frequencies (8 kHz or more). But all share the same core mechanism of fast muscular actuation of a springy membrane coupled
24
. This buckle–release cycle happens extremely
. The series of clicks from
. When the cicada contracts its
14
24
11
12
filled abdominal cavity (air sac) that acts like a Helmholtz resonator or echo chamber
12
. In essence, the tymbal provides the
25
. Research by Young and Bennet-Clark showed that for loud cicada
. The result is a louder and
11
12
26
. Bennet-Clark (1999) noted
. The biological design is ingenious: a small mechanical
26
27
4

## Slide 5
to an acoustic cavity. Any successful synthesis should respect this two-stage sound production: anexcitation source (bunch of pulses) into a band-limited resonator.
Applying Acoustic Analysis to WebAudio Synthesis
Recreating cicada calls with the Web Audio API will leverage the above insights – we know the targetspectral profile and temporal pattern for each species, and we have clues from modeling research on howto synthesize such sounds. The Web Audio API provides tools like oscillators, noise sources (viaAudioBuffer or ScriptProcessor/AudioWorklet), filters, and envelope control (Gain nodes) which can becombined to simulate the cicada sound mechanism. Here are key considerations and techniques:
• Band-Limited Source (Oscillators vs Noise): Cicada calls are not pure tones; they contain abroad cluster of frequencies. A simple sine OscillatorNode would be insufficient. Instead, considerusing a noise source filtered to the appropriate band. For example, to mimic Minminzemi,generate white noise and run it through a band-pass BiquadFilter centered around ~4–5 kHz witha bandwidth of a few kHz (to cover 3–6 kHz)
distributed like the cicada’s timbre. Farnell recommends heavily filtering the noise to confine it tothe insect’s frequency range (e.g. 5–8 kHz for many cicadas), because any excess low-frequencycontent can introduce rumbling or amplitude modulation artifacts that make the result lessrealistic
kHz, or a bimodal spectrum with a gap
single band-pass with a higher Q that is swept during the call. In WebAudio, you can also utilize
the PeriodicWave or add multiple OscillatorNodes to approximate harmonic bands, but a filterednoise approach more naturally yields the raspy, dense quality of cicada sound
1
. This creates a noisy signal with energy
18
. If a species has two distinct spectral peaks (e.g. Tsukutsukuboushi’s ~6 kHz and ~12
), you might use two band-pass filters in parallel, or a
2
16
.
• Amplitude Envelopes and Rhythm: The characteristic rhythm of each cicada must beprogrammed via gain envelopes or oscillator modulation. For continuous buzz species likeKumazemi, you might apply a subtle tremolo (amplitude modulation) at, say, 20–30 Hz tosimulate any fine flutter, but largely keep the Gain node open for a sustained “shaaa” duration. For
initial “Meeen” (perhaps a few hundred milliseconds long) immediately followed by a loop orsequence of shorter bursts for the “min-min-min”. In WebAudio, this can be achieved byscheduling GainNode gain changes with setValueAtTime and linearRampToValueAtTime to forma custom envelope, or by using a low-frequency OscillatorNode (set to a rhythmic frequency)connected to the gain. For example, Minminzemi’s repetition rate might be on the order of ~4–6cycles per second for the full call (each phrase ~0.2–0.3 s of sound followed by a pause)
Tsukutsukuboushi’s call can be scripted as a series of distinct segments: an intro section with onerhythm and frequency, then a crescendo section with a faster, higher-pitched rhythm. You couldmanually trigger these segments via the WebAudio start() times or use a single longer Gainenvelope that changes shape. Farnell’s analysis indicated a roughly 25 Hz modulation inside somecicada calls (i.e. bursts every 40 ms)
modulate gain or use a patterned buffer to impart that buzzing microstructure within each chirp.The key is to reproduce both the macro structure (overall call length and phrasing) and the micro
pulsed calls like Minminzemi, you can design a two-stage envelope: a longer attack-decay for the
19
.
19
– if needed, one can add a high-rate oscillator to
structure (the tremble or vibration within each phrase).
• Frequency Modulation and Sweeps: For species with changing pitch, like Tsukutsukuboushi,simply filtering noise may not capture the perceptible rise in pitch. In such cases, you mightintroduce an oscillator component mixed in or modulate the filter center frequency over time.For instance, during the “tsukutsukubōshi” call, you could start a bandpass filter at ~2 kHz andramp its center to ~8–10 kHz by the end of the call to mirror the spectrogram
2
. Alternatively,
5

## Slide 6
use two oscillators an octave or two apart to emphasize the tonal rise, or use Frequency Paramautomation on an OscillatorNode if generating a tonal backbone. The Web Audio API allowssmooth automation of frequencies on Oscillators and BiquadFilter nodes, which is useful forimitating the frequency glide in Tsukutsukuboushi’s second half
sweep matches the natural call (a few seconds from start to finish) will make the synthetic callmore convincing.
• Resonance and Filtering (the “Resonator” stage): To incorporate the effect of the cicada’sabdominal resonator, you can use filters to shape the timbral envelope of each pulse. A shortimpulse through a band-pass filter will ring for a few cycles – analogous to the tymbal clickexciting the air sac resonance. In practice, your noise burst or oscillator burst can be sculpted byone or two BiquadFilterNodes (configured as band-pass or high-Q peaking filters) tuned to theprimary frequencies of the species. For example, if analysis shows peaks at 6 kHz and 15 kHz forTsukutsukuboushi
factor) can be adjusted to control how “sharp” or bell-like the resonance is. A higher Q yields amore tonal ring (but too high might sound artificial), whereas a lower Q gives a broader noise-likecharacter. You may also modulate the filter’s gain or frequency slightly during the call to simulatethe effect of the cicada dynamically opening its opercula (changing the acoustic coupling) – incicada physiology, movements of the abdominal plates can alter the tone color
closing the opercula might dampen high frequencies (akin to a VCF closing). In synthesis, thiscould be an envelope that slightly reduces a filter’s cutoff or gain toward the end of a callsegment.
• Synthesis Architecture (Oscillator → Filter → Amplifier): Interestingly, the cicada’s soundproduction chain maps well to a subtractive synthesis architecture. As noted by Matsumura, thecicada’s tymbal is like a VCO (oscillator) producing a rapid vibration, the abdominal cavity is like a
akin to a VCF (filter) shaping the timbre
our “VCO”). This goes into one or more filters (band-pass filters simulating the resonant body –our “VCF”) to impose the tonal character. Finally, a GainNode acts as an amplitude envelope (the“VCA”), which we modulate to produce the call’s amplitude pattern. By separating these stages,you can fine-tune each: e.g. adjust the filter frequency to match the species (higher for smallercicadas, lower for large ones), and adjust the Gain envelope to get the right duty cycle (continuousvs. pulsed). This modular approach mirrors the physical reality and is supported by the Web Audiograph design.
In conclusion, faithfully reproducing cicada calls with WebAudio is achievable by combining analysis-
spectra, pulse rates, envelope shapes) as a blueprint: for example, we know Minminzemi’s energy isfocused around 4 kHz with an on-off envelope
matching gain pattern. We know cicada chirps result from impulses at high rates, so we opt for noise-based excitation filtered into chirps rather than a single tone
oscillators for any tonal components, noise for chaotic clicks, filters for resonance, and scheduled gainchanges for rhythm – one can synthesize remarkably life-like cicada songs in the browser. The key is torespect the natural structure (both spectral and temporal) that studies have identified for each species,thereby ensuring the essence of the cicada’s voice is captured in the synthetic version.
2
. Ensuring the timing of this
2
, you might boost those frequencies with filter nodes. The filter Q (quality
23
. For instance,
VCA (amplifier/resonator) boosting the sound, and the adjustable abdominal openings function
source can be an OscillatorNode generating a high-frequency click train or a noise burst (this is
28
. We can emulate this in WebAudio: The excitation
driven parameters with creative use of the API’s synthesis primitives. We use research data (frequency
1
, so we implement a 4 kHz-centered filter and a
. By iterating with these building blocks –
16
19
2
6

## Slide 7
Sources:
1
2
8
• Acoustic analyses of Japanese cicada calls (spectrogram data and frequency ranges)
• Smyth, T. & Smith, J. “A Musical Instrument Based on a Bioacoustic Model of a Cicada” – physicalmodel of cicada sound mechanism
• Matsumura, S. (2022). Physical Modeling Synthesis of Cicada Chirping – Pd implementation andanalogy to synthesizer architecture
• Farnell, A. Designing Sound (2010), Ch. 50 “Insects” – procedural synthesis of insect sounds;cicada noise-band model and modulation rates
• Bennet-Clark, H. C. & Young, D. (1994, 1999) – Bioacoustic studies on cicada tymbal mechanismand resonance (as cited in Smyth’s and Farnell’s work)
• Kyushu Univ. News (2023) “Biological meaning hidden in the key change of Tsukutsukuboushi’s
7
6
11
12
28
22
29
16
11
26
5
call” – ecological significance of two-part call pattern
1
2
4
夏の風物詩、セミの鳴き声を科学する！アブラゼミ,ミンミンゼミ,ツクツクボウシの“音を見える
化”してみた｜Sound One
❣
https://note.com/sound_one/n/n855133c10b73
3
6
27
セミの声の自由研究：スペクトルで見る暑苦しさと涼しさ | のんびりポタ・ランニング
https://pota-run.blogspot.com/2013/08/blog-post_3.html
5
ツクツクボウシの鳴き声の転調部に潜む生物学的意味 | 九州大学 理学研究院 理学府 理学部
https://www.sci.kyushu-u.ac.jp/koho/qrinews/qrinews_230908.html
7
セミの声 | 岩永補聴器グループのブログ
https://www.iwanaga-co.com/blog/isahaya/4206
8
計測情報メールマガジン 2020/08/31号 身の回りの音の可視化① セミの鳴き声と虫の声 | ペリテック 製品
販売・サービス
https://peritec-sales.com/news/news-917/
9
101112141526
A Musical Instrument Based on a Bioacoustic Model of a Cicada
https://quod.lib.umich.edu/cgi/p/pod/dod-idx/musical-instrument-based-on-a-bioacoustic-model-of-a-cicada.pdf?
c=icmc;idno=bbp2372.2001.063;format=pdf
1321222328
data.jssa.info
https://data.jssa.info/paper/2022v14n02/2.Matsumura.pdf
16171819202429
Designing Sound - Andy Farnell.pdf - PDFCOFFEE.COM
https://pdfcoffee.com/designing-sound-andy-farnellpdf-pdf-free.html
25
a model of the mechanism of sound production in cicadas
https://www.semanticscholar.org/paper/A-MODEL-OF-THE-MECHANISM-OF-SOUND-PRODUCTION-IN-Bennet-Clark-Young/
7c7b0869efb30e14a78f619158679cf18e03a1f7/figure/14
7